## Slide 1: Skagit Streamflow Visualization
Training for Seattle City Light Employees
Ronda Strauch, Crystal Raymond, and Christina Bandaragoda
February 13, 2020

## Slide 2: Agenda
1:30 Welcome
1:35 Purpose and Introduction to Project
1:40 Skagit Streamflow Modeling Overview
1:50 Streamflow Visualization Tool Overview
2:00 Tool Exercise
2:30 Exercise Review
2:50 Wrap-up & Survey

## Slide 3: “Streamflow For All”
Climate resilience
  co-produced & usable climate science
Focused on the Skagit
  Operations, relicensing, resource adequacy
Visualize and understand streamflow
  Historic and future, changes, uncertainty
What’s in it for you?
  Access tool, interact with data, visualize streamflow, download and share figures and data

## Slide 4
Skagit
Hydrologic
Modeling
Potential impacts of climate change on streamflows at 20 sites in the Skagit Watershed, stemming from the report prepared entitled: Hydrology, Stream Temperature and Sediment Impacts of Climate Change in the Sauk River Basin.
Dr. Christina Bandaragoda
Civil & Environmental Engineering
University of Washington, Seattle
Seattle City Light Workshop, February 13, 2020

## Slide 5: Hydrologic Modeling
South Fork of Sauk River viewed from foot bridge entering the Monte Cristo townsite by Junkyardsparkle. CC0 1.0 Public Domain.
DHSVM Grid
DHSVM Glaciers
Distributed hydrology, soil, & vegetation model with glacier dynamics at 3-hr timestep for 1969-2099. Every 150 m grid cell uses physical equations to simulate transport of water from high elevations with ice and snow processes to low elevations with canopy and soil processes. Wigmosta et al., (1994); Naz et al. (2011); Frans et al. (2013).

## Slide 6: Global Climate to Seattle City Light Model Workflow
Chain of models linking global emissions scenarios to hydrologic impacts in the Skagit River Basin. At the top, black boxes are products of CMIP5 (World Climate Research Programme's Working Group on Coupled Modelling (Taylor et al., 2012)); the next green box is a product developed by a collaboration of Oregon State University (OSU) and the University of Idaho (UI) (Abatzoglou and Brown, 2012); the following yellow boxes are tools and data developed in collaborations at the University of Washington (UW) (Wigmosta et al., 1994; Clarke et al., 2015; Naz et al., 2014); and the blue boxes are data inputs and outputs developed in collaboration during this project with Seattle City Light (SCL) and the Skagit Climate Science Consortium.
Updates May 2019
Hybrid Climate Data Correction
10
daily

## Slide 7: Meteorology Inputs
Interpolation from Weather Stations
DISTRIBUTED HYDROLOGY SOIL VEGETATION MODEL: DHSVM
Distributed hydrology & glacier dynamics
Snow density is tracked and produces ice.
Distributed solar forcing and 3-layer surface energy balance
Snow/ice melt & Evapotranspiration
Kinematic subsurface flow
Channel routing
2. Regional Climate Model:
interpolation from weather forecast model
“Livneh”
“WRF”

## Slide 8
Livneh
WRF
Local bias correction
Hybrid
TMAX <=0 33% 35% 33% 9%
TMIN <=0 64% 85% 64% 78%
Livneh
WRF
Local correction
Hybrid
P=2,760 mm
P=2,510 mm
P=2,800 mm
P=2,520 mm
Skagit River: November Mean Daily Tmax
Skagit River: Annual Mean Precipitation
Notes: Hybrid product get warmer

## Slide 9: Results – Seasonal Streamflow At Thunder Creek

## Slide 10: Supporting Data & Reports

## Slide 11: Sponsors
11
2016: Northwest Science Special Issue articles “Impact of Recent Glacial Recession on Summer Streamflow in the Skagit River,” “Impacts of Climate Change on Regulated Streamflow, Hydrologic Extremes, Hydropower Production, and Sediment Discharge in the Skagit River Basin,” and “Effects of Climate Change on Extreme Low-Flows in Small Lowland Tributaries in the Skagit River Basin.”
2019: Reported Model updates in Skagit
Bandaragoda, C., S. LEE, E. Istanbulluoglu, A. Hamlet (2020). Hydrology, Stream Temperature, and Sediment Impacts of Climate Change in the Sauk River Basin, HydroShare, http://www.hydroshare.org/resource/e5ad2935979647d6af5f1a9f6bdecdea
Please see the Data Sharing Agreement
https://www.hydroshare.org/resource/a3d213ce180a4fbeb7c354565c35fb87/
Electronic Digital Appendix with links to model, inputs, outputs, on HydroShare.
2015: Hydrologic Impacts of Climate Change in the Skagit River Basin Christina Bandaragoda, Chris Frans, Erkan Istanbulluoglu, Crystal Raymond and Larry Wasserman
VIEW ABSTRACT | VIEW REPORT
Photo by Ron Clauson

## Slide 12: Data Archived On HydroShare.org

## Slide 13: Sponsors
This project has been supported by the Bureau of Indian Affairs (BIA), an agency of the U.S. federal government within the U.S. Department of Interior responsible for administration and management of land held in trust by the U.S for Native Americans in the United States. The contents of this document do not necessarily reflect the views and policies of the BIA, nor does mention of trade names or commercial products constitute endorsement or recommendation for use.
This project has been supported by the Department of Civil & Environmental Engineering and the College of Engineering at the University of Washington.
This project was made possible in part by the Skagit Climate Science Consortium, a 501 c(3) nonprofit comprised of a group of member research scientists from federal, state, municipal, tribal, university, and non-governmental organizations who work in the Skagit basin.
Early support project has been funded in part by the Climate Change Research Initiative, Seattle City Light, a public utility that serves the City of Seattle.
Early support for this project has been funded in part by the United States Environmental Protection Agency under Assistance Agreement to the Swinomish Indian Tribal Community and to the Sauk-Suiattle Indian Tribe. The contents of this document do not necessarily reflect the views and policies of the Environmental Protection Agency, nor does mention of trade names or commercial products constitute endorsement or recommendation for use.
13

## Slide 14: Skagit Streamflow – Let’s Explore!

## Slide 15: Skagit Climate Change And Streamflow Visualization
Data for 20 streamflow locations
Projected changes in monthly average streamflow
Projected changes in peak and low streamflow extremes
Projected Future Streamflow
  Timeframe: 2010 – 2099
  20 climate models
  Two greenhouse gas scenarios (low and high)
Visualization designed for easy exploration of data

## Slide 16: Skagit Climate Change And Streamflow Visualization
http://www.skagitclimatescience.org/projected-changes-in-streamflow/

## Slide 17
Exercise 1. review

## Slide 18
Exercise 2. review

## Slide 19
Exercise 3. Review

## Slide 20
Exercise 4. Review

## Slide 21: We don’t like Surprises
Photo Credit: Yongquing Bao Tibetan fox and marmot at Chana’s Qilian Mountains National Nature Reserve
Questions?
Thank You!